## Slide 1
Unit 11 Memory Operation and Performance
李靓 (Li Jing) lijing712@scu.edu.cn
School of Computer Science / Software Engineering
System Level Programming

## Slide 2
11.0 Review
11.1 Memory Technology [CSAPP 6.1]
11.2 Memory Hierarchies [CSAPP 6.3]
11.3 Locality [CSAPP 6.2]
11.4 Memory Mountain Lab [CSAPP 6.6]
Memory Operation and Performance

## Slide 3
The module of CS that have been using until now
11.0 Review
Processor
Memory
ALU
Step 1. Fetch instruction
Step 3. Execute instruction
Step 4. Store results
Control Unit
Step 2. Decode instruction

## Slide 4
The module of CS that have been using until now
11.0 Review
Control logic
Address bus
Data bus
Control circuit
Instruction decoder
Memory
Address decoder
Control bus
BUS

## Slide 5
11.0 Review
11.1 Memory Technology [CSAPP 6.1]
11.2 Memory Hierarchies [CSAPP 6.3]
11.3 Locality [CSAPP 6.2]
11.4 Memory Mountain Lab [CSAPP 6.6]
Memory Operation and Performance

## Slide 6
11.1.1 Random-Access Memory (RAM)
11.1.2 Read only Memory (ROM)
11.1.3 Disk Storage
11.1.4 SSD/Flash
11.1.5 Storage Technology Trends
11.1 Memory Technology

## Slide 7
Random-Access Memory (RAM)
  Random-Access
  Volatile (易失性)
11.1.1 Random-Access Memory (RAM)

## Slide 8
RAM comes in two varieties
  SRAM (Static RAM)
  DRAM (Dynamic RAM)
11.1.1 Random-Access Memory (RAM)
 | Tran. per bit | Access time | Needs refresh? | Sensitive? | Cost | Applications
SRAM | 6 | 1X | No | No | 100X | Cache memories
DRAM | 1 | 10X | Yes | Yes | 1X | Main memories Frame buffers

## Slide 9
DRAM (Dynamic RAM)
  Each cell stores one bit
  Transistor (晶体管) + Capacitor (电容) [1T1C]
  Refreshed every 10-100 ms
11.1.1 Random-Access Memory (RAM)
Word line
Bit line

## Slide 10
SRAM (Static RAM)
  Each cell stores one bit
  6-transistor circuit
11.1.1 Random-Access Memory (RAM)

## Slide 11
Key features - outside
  Traditionally packaged as a chip
  Multiple RAM chips form a memory
  SIMM (Single Inline Memory Module) 单列直插内存模块
  DIMM (Dual Inline Memory Module) 双列直插内存模块
11.1.1 Random-Access Memory (RAM)

## Slide 12
Key features – inside
  Cell
  Supercell
  Module
11.1.1 Random-Access Memory (RAM)
8 bits Supercell

## Slide 13
Multiple Cells -> Supercell
11.1.1 Random-Access Memory (RAM)
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 14
11.1.1 Random-Access Memory (RAM)
Step 1(a): Row Access Strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2 bits
/
8 bits
/
Memory
controller

## Slide 15
11.1.1 Random-Access Memory (RAM)
Step 2(a): Column Access Strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied form buffer to data lines, and eventually back to CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
CAS = 1
addr
data
2 bits
/
8 bits
/
Memory
controller
supercell
(2,1)
To CPU
supercell
(2,1)

## Slide 16
Multiple Supercells -> Module
11.1.1 Random-Access Memory (RAM)
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit word
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 17
CPU access RAM via traditional BUS structure
  A collection of parallel wires that carry address, data, and control signals.
  Typically shared by multiple devices.
11.1.1 Random-Access Memory (RAM)
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 18
What can the memory controller do?
  Address to RAS and CAS
  Control the transactions of memory
  Buffer
11.1.1 Random-Access Memory (RAM)
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
A memory controller inside

## Slide 19
Memory read transaction
  Load operation
11.1.1 Random-Access Memory (RAM)
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
mov eax, [A]

## Slide 20
Memory read transaction (1)
  CPU places address A on the bus
11.1.1 Random-Access Memory (RAM)
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
mov eax, [A]

## Slide 21
Memory read transaction (2)
  Main memory read A from the bus, retrieves word x, and places it on the bus
11.1.1 Random-Access Memory (RAM)
ALU
Register file
Bus interface
x
0
A
x
Main memory
%eax
I/O bridge
mov eax, [A]

## Slide 22
Memory read transaction (3)
  CPU read word x from the bus and copies it to register eax
11.1.1 Random-Access Memory (RAM)
x
ALU
Register file
Bus interface
x
Main memory
0
A
%eax
I/O bridge
mov eax, [A]

## Slide 23
Memory write transaction
  Store operation
11.1.1 Random-Access Memory (RAM)
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
mov [A], eax

## Slide 24
Memory write transaction (1)
  CPU places address A on bus. Main memory reads it and waits for corresponding data
11.1.1 Random-Access Memory (RAM)
y
ALU
Register file
Bus interface
A
Main memory
0
A
%eax
I/O bridge
mov [A], eax

## Slide 25
Memory write transaction (2)
  CPU places data y on the bus
11.1.1 Random-Access Memory (RAM)
y
ALU
Register file
Bus interface
y
Main memory
0
A
%eax
I/O bridge
mov [A], eax

## Slide 26
Memory write transaction (3)
  Main memory read data y from the bus and stores it at address A
11.1.1 Random-Access Memory (RAM)
y
ALU
Register file
Bus interface
y
main memory
0
A
%eax
I/O bridge
mov [A], eax

## Slide 27
Enhanced DRAMs
11.1.1 Random-Access Memory (RAM)
FPM DRAM
快页模式
EDO DRAM
扩展数据输出
SDRAM
同步DRAM
RDRAM
Rambus DRAM
DDR SDRAM
双倍速率SDRAM
DDR2/DDR3 SDRAM

## Slide 28
11.1.1 Random-Access Memory (RAM)
11.1.2 Read only Memory (ROM)
11.1.3 Disk Storage
11.1.4 SSD/Flash
11.1.5 Storage Technology Trends
11.1 Memory Technology

## Slide 29
Read Only Memory (ROM) – key features
  Nonvolatile (非易失性)
  Read only
Types
  PROM (可编程)
  EPROM (可擦除可编程)
  EEPROM (电可擦除可编程)
  Flash (U disk, cell phone, digital camera…)
11.2 Read only Memory (ROM)

## Slide 30
Firmware
  Program stored in ROM
    Boot time code such as BIOS
    Graphics card BIOS
    Disk controller
    Wireless network card
11.2 Read only Memory (ROM)

## Slide 31
11.1.1 Random-Access Memory (RAM)
11.1.2 Read only Memory (ROM)
11.1.3 Disk Storage
11.1.4 SSD/Flash
11.1.5 Storage Technology Trends
11.1 Memory Technology

## Slide 32
Disk
  Hard disk
    IDE/SATA
    SCSI
11.1.3 Disk Storage
C:或D: 1TB、2TB

## Slide 33
What’s inside a disk driver
11.1.3 Disk Storage
Spindle 主轴
Arm 机械手臂
Platters 盘片
Main control chip
主控芯片
(including a
processor
and memory!)
Connector
外部接口

## Slide 34
Inside static
  Platters | Surfaces | Tracks | Sectors | Gaps
11.1.3 Disk Storage
磁道 Track
面 Surface
面 Surface
扇区 Sector
track k
sectors
gaps

## Slide 35
Inside static
11.1.3 Disk Storage
Cylinder 柱面
Platter 0
Platter 1
Platter 2
Head 磁头
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5

## Slide 36
Capacity (容量) is the maximum number of bits that can be stored
  Usually in GB (GigaBytes), TB (TeraByte )
Related factors
  Recording density (bits/inch segment of a track)
  Track density (tracks/inch radial segment)
  Areal density (bits/in2) Product of the above
11.1.3 Disk Storage

## Slide 37
Modern disks
  Recording zones
  Average number of sectors/tracks when computing capacity
11.1.3 Disk Storage
  Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
…
Spindle

## Slide 38
Example
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB
11.1.3 Disk Storage

## Slide 39
Disk operation
11.1.3 Disk Storage
The disk surface
spins at a fixed
rotational rate
spindle
spindle
spindle
spindle
spindle

## Slide 40
Disk access - Read
11.1.3 Disk Storage
About to read blue sector

## Slide 41
Disk access - Read
11.1.3 Disk Storage
After BLUE read
After reading blue sector

## Slide 42
Disk access - Read
11.1.3 Disk Storage
After BLUE read
Red request scheduled next

## Slide 43
Disk access - Seek
11.1.3 Disk Storage
After BLUE read
Seek for RED
Seek to red’s track

## Slide 44
Disk access – Rotational latency
11.1.3 Disk Storage
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around

## Slide 45
Disk access - Read
11.1.3 Disk Storage
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red

## Slide 46
Disk access – Service time component
11.1.3 Disk Storage
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer

## Slide 47
Disk access time
  Average time to access some target sector
  Seek time 寻道时间
    Typically it takes 3-9 ms
  Rotational latency time 旋转延迟
    7200 RPM (Revolutions Per Minute)
  Transfer time 传输时间
11.1.3 Disk Storage

## Slide 48
Given
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms
  Avg # sectors/track = 400
Derived
11.1.3 Disk Storage

## Slide 49
CPU access disk
  Bus and I/O ports
  DMA and interrupt
11.1.3 Disk Storage

## Slide 50
11.1.3 Disk Storage
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.
Load from disk to memory

## Slide 51
11.1.3 Disk Storage
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
Command = logical block number + destination memory address to a port (address) associated with disk controller.

## Slide 52
11.1.3 Disk Storage
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 53
11.1.3 Disk Storage
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 54
Logical disk blocks in modern disks
  An abstract of the complex sector geometry
  A sequence of b-sized logical blocks (0,1,2,…)
Mapping 映射
  Maintained by disk controller
  Logical block (0,1,2,…) -> (surface, track, sector)
Allows controller to set aside spare cylinder for each zone
  “formatted capacity” and “maximum capacity”
11.1.3 Disk Storage

## Slide 55
What can disk controller do?
  Logical blocks -> physical blocks of CHS
  Control operations on the disk
  Buffer
  Interrupt
11.1.3 Disk Storage

## Slide 56
11.1.1 Random-Access Memory (RAM)
11. 1.2 Read only Memory (ROM)
11.1.3 Disk Storage
11.1.4 SSD/Flash
11.1.5 Storage Technology Trends
11.1 Memory Technology

## Slide 57
Solid State Disks (SSDs)
11.1.4 SSD/Flash
Flash
translation layer
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
I/O bus
Pages: 4KB, 8KB, or 16KB | Blocks: 32, 64, 129 or 256
Data read/written in units of pages.
Page written only when its block been erased
A block wears out after about 100,000 repeated writes

## Slide 58
SSD performance characteristics
  Sequential access faster than random access
  Why are random writes so slow?
11.1.4 SSD/Flash
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg seq read time 50 us Avg seq write time 60 us
  Pages cannot be overwritten when modifying a page
  Erasing a block triggered by GC takes a long time (~1 ms)

## Slide 59
Random writes
11.1.4 SSD/Flash
Write page H
Modify page G

## Slide 60
Random writes
11.1.4 SSD/Flash
Garbage collection

## Slide 61
SSD tradeoffs V.S. Rotating disks
Advantages
  No arm -> Faster, less power, more rugged
Disadvantages
  The potential to ware out
  About 30 times more expensive per byte in 2015
Applications
  Smart phones, laptops
  Desktops and servers
11.1.4 SSD/Flash

## Slide 62
11.1.1 Random-Access Memory (RAM)
11. 1.2 Read only Memory (ROM)
11.1.3 Disk Storage
11.1.4 SSD/Flash
11.1.5 Storage Technology Trends
11.1 Memory Technology

## Slide 63
Storage trends
11.1.5 Storage Technology Trends

## Slide 64
CPU clock rate
11.1.5 Storage Technology Trends

## Slide 65
The CPU-MEMORY gap
11.1.5 Storage Technology Trends
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk
SRAM

## Slide 66
11.0 Review
11.1 Memory Technology [CSAPP 6.1]
11.2 Memory Hierarchies [CSAPP 6.3]
11.3 Locality [CSAPP 6.2]
11.4 Memory Mountain Lab [CSAPP 6.6]
Memory Operation and Performance

## Slide 67
Design constraints of a computer’s memory
Balance among (Speed, Price, Capacity)
  Faster access time but smaller capacity
  Greater capacity but more expensive per bit
  Smaller cost per bit but slower access speed
Trade off – To use them all in hierarchy
11.2 Memory Hierarchies
How many | How fast | How much
Capacity | Speed | Price
Larger | Faster (= CPU) | Lower

## Slide 68
11.2 Memory Hierarchies

## Slide 69
Why do memory hierarchies work?
  Programs tend to access data at level k more often than they access data at level k+1
  Storage at level k+1 can be slower, thus larger and cheaper per bit
Fundamental idea
  Level k serves as a cache for level k+1
  Level k+1 serves as a backup for level k
11.2 Memory Hierarchies

## Slide 70
11.2 Memory Hierarchies
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Level k+1
Data is copied in block-sized transfer units
Level k
4
4
4
10
10
10

## Slide 71
Cache hit
11.2 Memory Hierarchies
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 72
Catch miss
11.2 Memory Hierarchies
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 73
Types of cache misses
Code (compulsory) miss
  When cache is empty
Capacity miss
  When active cache blocks is larger than cache
Conflict miss
  Cache limit blocks at level k+1 to a small subset of the block positions at level k
  i mod 4
  Reference blocks 0,2,0,2,0,2,…
11.2 Memory Hierarchies

## Slide 74
Policy, related to transfer between two levels
11.2 Memory Hierarchies

## Slide 75
Examples of caching in memory hierarchy
11.2 Memory Hierarchies
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 76
11.0 Review
11.1 Memory Technology [CSAPP 6.1]
11.2 Memory Hierarchies [CSAPP 6.3]
11.3 Locality [CSAPP 6.2]
11.4 Memory Mountain Lab [CSAPP 6.6]
Memory Operation and Performance

## Slide 77
Transferring block between levels cost time
  Have the data already in fast memory by the time CPU actually requests it
  How to fulfill this goal?
11.3 Locality

## Slide 78
Principle of locality
  Programs tend to use data and instructions with addresses near or equal to those they have used recently
Locality is an attribute of program that
  Programs with good locality run faster
Locality is important to
  Memory hierarchy
  Hardware design
  Software design (To make programs with better locality)
11.3 Locality

## Slide 79
Types
Temporal locality
  Recently referenced items
  are likely to be referenced
  again
Spatial locality
  Items with nearby addresses
  tend to be referenced close
  together in time
11.3 Locality

## Slide 80
Example
Assume
  MAX = 2
  Starting address for instructions is FRAG
  Local variable sum and i are at addresses STACKPTR+X and STACKPTR+X+4
  Global variable array is at address ARRAY
11.3 Locality
sum = 0;
for (i = 0; i < MAX; i++)
sum += array[i];

## Slide 81
11.3 Locality
sum = 0;
for (i = 0; i < MAX; i++)
sum += array[i];

## Slide 82
11.3 Locality

## Slide 83
11.3 Locality

## Slide 84
11.3 Locality

## Slide 85
11.3 Locality

## Slide 86
11.3 Locality

## Slide 87
Conclusion
11.3 Locality
sum = 0;
for (i = 0; i < MAX; i++)
sum += array[i];
Data references
  - Reference array elements array[i] in succession.
  - Reference variable sum each iteration.
Instruction references
  - Reference instructions in sequence.
  - Cycle through loop repeatedly.
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 88
Repeatedly reference the same variable enjoy good temporal locality
Stride-k reference patterns enjoy good spatial locality with smaller strides
Loops have good spatial and temporal locality with respect to instruction fetches with smaller loop body and greater number of loop iterations
11.3 Locality

## Slide 89
11.0 Review
11.1 Memory Technology [CSAPP 6.1]
11.2 Memory Hierarchies [CSAPP 6.3]
11.3 Locality [CSAPP 6.2]
11.4 Memory Mountain Lab [CSAPP 6.6]
Memory Operation and Performance

## Slide 90
11.4 Memory Mountain Lab

## Slide 91
Ridges of Temporal Locality: Slice through the memory mountain with stride=1
11.4 Memory Mountain Lab

## Slide 92
A Slope of Spatial Locality: Slice through memory mountain with size=256KB
11.4 Memory Mountain Lab

## Slide 93
11.4 Memory Mountain Lab