## Slide 1
Unit 12 Catch and Catch-Aware Programming
李靓 (Li Jing) lijing712@scu.edu.cn
School of Computer Science / Software Engineering
System Level Programming

## Slide 2
12.0 Introduction
12.1 Catch types according to implementation
12.2 Writing catching friendly code and catch-aware optimization
Catch and Catch-Aware Programming

## Slide 3
12.0 Introduction

## Slide 4
Examples of caching in memory hierarchy
12.0 Introduction
Hardware
MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 5
12.0 Introduction
Miss rate
  H = No.Miss / No.Ref
  Cold miss
  Conflict miss (Thrash)
  Capacity miss
Hit rate
  1 – H
Hit time
Miss penalty
Spatial locality
Temporal locality
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Level k+1
Level k
4
4
4
10
10
10

## Slide 6
What cache means?
  Broad sense: level k and level k+1
    Cache | Memory | Disk | Server
  Narrow sense: small, fast memory between the CPU registers and the main memory
    Cache - SRAM
    Managed by hardware logic
12.0 Introduction

## Slide 7
Intel Pentium III Cache
Concluding observations

## Slide 8
Basic policy that should be concerned
Cache size
Block size
Miss or hit
Pre-fetch or demand fetch
Placement
Replacement
  FIFO, LRU, LFU
Write/update
  Write through 直写
  Write back 写回
12.0 Introduction
4
9
14
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
cache
memory

## Slide 9
Many kinds of cache
  By level – L1, L2, …
  By content – data, instruction
  By on chip or not
  By implementation – Organization
12.0 Introduction

## Slide 10
12.0 Introduction
12.1 Catch types according to implementation
12.2 Writing catching friendly code and catch-aware optimization
Catch and Catch-Aware Programming

## Slide 11
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 12
Where can a block be placed in a cache?
  Direct mapped (直接映射): Each block has only one place it can appear in the cache.
  Set associative (组相联): A block can be placed in a restricted set of places. (2-way, 4-way, 8-way, etc.)
  Fully associative (全相联): A block can be placed anywhere in the cache.
12.1.0 Introduction

## Slide 13
Generic cache memory organization
12.1.0 Introduction

## Slide 14
Address
12.1.0 Introduction
Process:
s bits -> t bits -> b bits
组选择+行匹配+字提取

## Slide 15
12.1.0 Introduction

## Slide 16
12.1.0 Introduction

## Slide 17
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 18
Organization
  Characterized by exactly one line per set
12.1.1 Direct Mapped Cache

## Slide 19
Addressing direct mapped cache
  Set index
12.1.1 Direct Mapped Cache

## Slide 20
Addressing direct mapped cache
  Line matching - find valid line
  Word selection
12.1.1 Direct Mapped Cache

## Slide 21
12.1.1 Direct Mapped Cache

## Slide 22
Example: 4-bit address for direct-mapped cache
  Cache set size = ?
  Size of the cache line = ?
12.1.1 Direct Mapped Cache
The Cache set size: N = 2s = 4
The size of the cache line: L = 2 b = 2 byte

## Slide 23
Example: 4-bit address for direct-mapped cache
12.1.1 Direct Mapped Cache
x
t=1
s=2
b=1
xx
x
Initially, the cache is empty (i.e., each valid bit is 0).
Read word at address 0 [0000].
Cache miss
Read word at address 1 [0001].
Cache hit
Read word at address 13 [1101].
Cache miss

## Slide 24
Example: 4-bit address for direct-mapped cache
12.1.1 Direct Mapped Cache
Read word at address 8 [1000].
Cache miss
Read word at address 0 [0000].
Cache miss

## Slide 25
Why use middle bits as set index?
  High-order bit indexing
  Adjacent memory lines
  map to same cache entry
  Poor use of spatial locality
12.1.1 Direct Mapped Cache
4-set cache

## Slide 26
Why use middle bits as set index?
  Middle-order bit indexing
  Consecutive memory lines
  map to different cache lines
  Hold C-byte region of address
  space in cache at one time
12.1.1 Direct Mapped Cache
4-set cache

## Slide 27
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 28
Organization
  Characterized by only one set
12.2.2 Fully Associative Cache
C = cache size
B = block size

## Slide 29
Accessing fully associative caches
  Set selection (No need)
12.2.2 Fully Associative Cache
The entire cache is one set, so by default set 0 is always selected

## Slide 30
Accessing fully associative caches
  Line matching
  Word selection
12.2.2 Fully Associative Cache

## Slide 31
12.2.2 Fully Associative Cache
全相连联像
15块
标记
…
…
1块
标记
0块
标记
Cache
11位
2047块
…
15块
…
1块
0块
主存
主存地址
块内偏移
主存块标记
9位
11位
主存块号
Cache大小是8k：有16个块，一个块的大小是512 byte
内存大小是1M： 有2048个块，一个块的大小是512 byte

## Slide 32
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 33
Organization
  Characterized by more than one line per set
12.1.3 Set Associative Cache

## Slide 34
Accessing set associative caches
  Set selection
12.1.3 Set Associative Cache

## Slide 35
Accessing set associative caches
  Line matching
  Word selection
12.1.3 Set Associative Cache

## Slide 36
12.1.3 Set Associative Cache
Cache大小是8k：有16个块，一个块的大小是512 byte
内存大小是1M： 有2048个块，一个块的大小是512 byte
2块
标记
3块
标记
…
…
15块
标记
14块
标记
1块
标记
0块
标记
Cache
8位
2047块
…
2041块
2040块
…
15块
…
9块
8块
7块
…
1块
0块
主存
…
0组
1组
7组
Cache组号
3位
7位
块内偏移
组内块号
9位
1位
Cache地址
主存块标记

## Slide 37
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 38
CSAPP 6.4.5: Issues with writes
  Write through VS Write back
  Write allocate VS Not write allocate
CSAPP 6.4.7: Performance impact of cache parameters
  Cache size
  Block size
  Association
  Writing strategy
12.1.4 Other Related Issues
4
9
14
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
cache
memory

## Slide 39
CSAPP 6.4.6: Instruction caches and unified caches
  Intel Core i7 Cache
12.1.4 Other Related Issues

## Slide 40
12.1.0 Introduction
12.1.1 Direct Mapped Cache
12.2.2 Fully Associative Cache
12.1.3 Set Associative Cache
12.1.4 Other Related Issues
12.1.5 An Example of Using Multi-level Cache
12.1 Catch types according to implementation

## Slide 41
Example code
12.1.5 An Example of Using Multi-level Cache
/* Assumes n is a power of two */
void merge_sort (int * data, int n) {
int half = n >> 1;
if (n == 1) return;
merge_sort(data, half);
merge_sort(data + half, half);
merge(data, data + half, half);
}

## Slide 42
Data using example, showing by figure
  Memory access: 32 times
12.1.5 An Example of Using Multi-level Cache

## Slide 43
Assuming that
  The caches are fully associative
  LRU is used for replacement
  The access times for each level of cache
    L1 cache (T1)
    L2 cache (T2)
    L3 cache (T3)
    Memory (Tm)
12.1.5 An Example of Using Multi-level Cache

## Slide 44
12.1.5 An Example of Using Multi-level Cache

## Slide 45
12.1.5 An Example of Using Multi-level Cache

## Slide 46
12.1.5 An Example of Using Multi-level Cache

## Slide 47
Assume
  T1 = 2 ns, T2 = 4 ns, T3 = 6 ns, Tm = 60 ns
Access time:
  for the one small L1 cache case
    Execution Time = (32-24)*T1 + 24* Tm = 1456 ns
  for the one large L3 cache case
    Execution Time = (32-8)*T3 + 8*Tm = 624 ns
  for the three-cache case
    Execution Time = (32-24)*T1 + (24-16)*T2 + (16-8)*T3 + 8*Tm = 574 ns
12.1.5 An Example of Using Multi-level Cache

## Slide 48
12.0 Introduction
12.1 Catch types according to implementation
12.2 Writing catching friendly code and cache-aware optimization
Catch and Catch-Aware Programming

## Slide 49
12.2.0 Introduction
12.2.1 Case1: Instruction cache overflow
12.2.2 Case2: Cache Collisions
12.2.3 Case3: Insufficient spatial locality
12.2.4 Case4: Insufficient temporal locality
12.2 Writing catching friendly code and cache-aware optimization

## Slide 50
CPU+MEMORY in CS
12.2 Writing catching friendly code and cache-aware optimization

## Slide 51
Notice
  Increase the locality of a program
  Efficiency V.S. Locality
    E.g. Loops
  Perform differently on different computers
12.2 Writing catching friendly code and cache-aware optimization

## Slide 52
12.2.0 Introduction
12.2.1 Case1: Instruction cache overflow
12.2.2 Case2: Cache Collisions
12.2.3 Case3: Insufficient spatial locality
12.2.4 Case4: Insufficient temporal locality
12.2 Writing catching friendly code and catch-aware optimization

## Slide 53
A program involving 3 complicated operations
  Bad temporal locality for big loop body
  If instructions in loop body overflow L1 instruction cache
12.2.1 Case1: Instruction cache overflow
for (i = 0; i < MAX; i++)
{
<Complicated operation on A[i]>
<Complicated operation on B[i]>
<Complicated operation on C[i]>
}

## Slide 54
12.2.1 Case1: Instruction cache overflow
for (i = 0; i < MAX; i++)
{
<Complicated operation on A[i]>
}
for (i = 0; i < MAX; i++)
{
<Complicated operation on B[i]>
}
for (i = 0; i < MAX; i++)
{
<Complicated operation on C[i]>
}

## Slide 55
12.2.0 Introduction
12.2.1 Case1: Instruction cache overflow
12.2.2 Case2: Cache Collisions
12.2.3 Case3: Insufficient spatial locality
12.2.4 Case4: Insufficient temporal locality
12.2 Writing catching friendly code and cache-aware optimization

## Slide 56
Cache collision [conflict miss]
12.2.2 Case2: Cache Collisions
int a[N];
<other stuff...>
int b[N];
<other stuff...>
int c[N];
for (i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}

## Slide 57
12.2.2 Case2: Cache Collisions
#define CACHELINESIZE <Cache line size of system>
#define COFFSET ((2 * CACHELINESIZE) / sizeof(int))
int a[N];
<other stuff...>
int b[N];
<other stuff...>
int c[N + COFFSET];
for (i = 0; i < N; i++) {
c[i + COFFSET] = a[i] + b[i];
}

## Slide 58
12.2.0 Introduction
12.2.1 Case1: Instruction cache overflow
12.2.2 Case2: Cache Collisions
12.2.3 Case3: Insufficient spatial locality
12.2.4 Case4: Insufficient temporal locality
12.2 Writing catching friendly code and cache-aware optimization

## Slide 59
Linear array
12.2.3 Case3: Insufficient spatial locality
int i;
int sum=0;
int data[ARRAY_SIZE]; // 4 bytes
for (i = 0; i < ARRAY_SIZE; i += stride)
sum += data[i];
32 bytes
Cache line
size
P1: 7/8
P2: all miss

## Slide 60
Two-dimensional array
  C arrays allocated in row-major order
12.2.3 Case3: Insufficient spatial locality
Row-major order
Column-major order
Data

## Slide 61
Two-dimensional array – focus on inner loop
12.2.3 Case3: Insufficient spatial locality
int data[M][N];
for (i = 0; i < M; i++) { //row
for (j = 0 ; j < N; j++) { // col
sum += data[ i ] [ j ];
}
}
int data[M][N];
for (j = 0 ; j < N; j++) { // col
for (i = 0; i < M; i++) { // row
sum += data[ i ] [ j ];
}
}

## Slide 62
Matrix multiply AB
12.2.3 Case3: Insufficient spatial locality

## Slide 63
Matrix multiply AC
12.2.3 Case3: Insufficient spatial locality

## Slide 64
Matrix multiply BC
12.2.3 Case3: Insufficient spatial locality

## Slide 65
Matrix multiply - Assume
  Data type: double
  Line size = 32B (big enough for 64b words)
  N is large enough (1/N is approximate to 0)
12.2.3 Case3: Insufficient spatial locality
 | Loads / iter | Stores / iter | A-miss / iter | B-miss / iter | C-miss / iter | Total-miss / iter
ijk&jik (AB) | 2 | 0 | 0.25 | 1.00 | 0.00 | 1.25
jki&kji (AC) | 2 | 1 | 1.00 | 0.00 | 1.00 | 2.00
kij&ikj (BC) | 2 | 1 | 0.00 | 0.25 | 0.25 | 0.50

## Slide 66
Matrix multiply – Pentium III Xeon
12.2.3 Case3: Insufficient spatial locality
AB
BC
AC

## Slide 67
Matrix multiply – Core i7
12.2.3 Case3: Insufficient spatial locality
AB
BC
AC

## Slide 68
12.2.0 Introduction
12.2.1 Case1: Instruction cache overflow
12.2.2 Case2: Cache Collisions
12.2.3 Case3: Insufficient spatial locality
12.2.4 Case4: Insufficient temporal locality
12.2 Writing catching friendly code and cache-aware optimization

## Slide 69
When we can do nothing to spatial locality
12.2.4 Case4: Insufficient temporal locality
int original[M][N];
int transposed[N][M];
for (i = 0; i < M; i++) {
for (j = 0; j < N; j++) {
transposed[i][j] = original[j][i];
}
}

## Slide 70
Idea – blocking for hit ratio improvement
12.2.4 Case4: Insufficient temporal locality

## Slide 71
12.2.4 Case4: Insufficient temporal locality

## Slide 72
Another example of matrix multiply
  For 8*8 matrix multiply, we could partition each matrix into four 4*4 submatrices
12.2.4 Case4: Insufficient temporal locality

## Slide 73
Another example of matrix multiply
12.2.4 Case4: Insufficient temporal locality

## Slide 74
Locality
12.2.4 Case4: Insufficient temporal locality

## Slide 75
Performance
12.2.4 Case4: Insufficient temporal locality